## Slide 1: AI-Driven Spatio-Temporal Traffic Intelligence System for Traffic Forecasting and Congestion Optimization
Phase-1 PBL Presentation
Team: [names] | Guide: [name] | [College, Dept.]
Notes: Introduce the project title, team and guide. One sentence: we forecast traffic speed on every road of a region for the next hour and use the forecast to recommend less-congested routes. Fill in the team line on this slide before presenting.

## Slide 2: Abstract
Traffic congestion in large Indian cities such as Bengaluru is usually noticed only after it has formed. This project builds a system that forecasts the traffic speed on each road of a region for the next 15, 30 and 60 minutes from historical data, then uses the forecasts to recommend less-congested routes and to raise early congestion alerts.
Roads are modelled as a graph, so that a jam on one road can inform the prediction for the roads it feeds. We compare simple baselines (historical average, gradient boosting, LSTM) with spatio-temporal graph neural networks (Graph WaveNet, STID) on the public METR-LA and PEMS-BAY benchmarks and on our own Bengaluru Outer Ring Road dataset, collected around the clock since 27 September 2026.
Models are evaluated with MAE, RMSE and MAPE on a chronological train, validation and test split.
21
road stretches collected around the clock
15 | 30 | 60
minute forecast horizons
3
datasets: METR-LA, PEMS-BAY and our Bengaluru corridor
Notes: Read the abstract in your own words, in about 40 seconds. The three numbers on the right: 21 stretches are being collected now; we forecast at three horizons; we use two public benchmarks and one local dataset. No results are claimed yet: Phase-1 is problem, literature and data.

## Slide 3: Introduction
Traffic has rhythms and shocks
Daily and weekly peaks, plus rain, accidents and events that no timetable predicts.
Roads form a network
A jam on one road slows the roads that feed it, so no road can be forecast alone.
Knowing ahead changes decisions
A forecast 30 to 60 minutes ahead lets commuters re-route and authorities act early.
5 km/h
against 39 km/h free-flow
Outer Ring Road near Agara (eastbound), 10:40 IST, 30 September 2026. Source: our own TomTom readings.
Our project: forecast speed on every road of a region for the next hour, then use the forecast to recommend routes and warn about congestion.
Notes: Three reasons forecasting matters: traffic has patterns and shocks, roads are connected, and early knowledge changes decisions. The callout is real data from our own collector: at 10:40 IST on 30 September the eastbound Outer Ring Road near Agara moved at 5 km/h where free-flow is 39 km/h.

## Slide 4: Existing System
Navigation apps
Google Maps, Waze and TomTom show live speeds from phone and vehicle GPS traces and estimate arrival times.
Limitation
The models are proprietary: they cannot be inspected, tested or tuned for a study region.
Signal control
Bengaluru has 405 signalised junctions; adaptive control (BATCS) ran at 169 of them by April 2025 (news reports).
Limitation
It manages junctions, not drivers' route choice, and signal plans are not public.
Classical forecasting
Historical average, ARIMA and SVR forecast each road's speed from its own past.
Limitation
They ignore the road network, and error grows with horizon (ARIMA on METR-LA: 3.99 mph MAE at 15 min, 6.90 at 60).
Gap: none of these combines network-aware forecasts with route choice, openly, for a chosen region.
Notes: Three families of existing systems. Navigation apps are good but closed. Signal control in Bengaluru works at junctions (405 signalised, adaptive at 169 by April 2025, per news reports) and does not advise drivers. Classical statistical forecasting treats every road alone and degrades quickly with horizon. The gap is the combination: network-aware forecasts plus route choice, open and testable.

## Slide 5: Problem Statement
“AI-Driven Spatio-Temporal Traffic Intelligence System for Traffic Forecasting and Congestion Optimization”
Forecast
Past T steps of speed at N connected road stretches
Spatio-temporal graph model
Next T' steps at all N stretches
Optimise
Predicted speed gives travel time: length ÷ speed
Dijkstra finds the fastest route
Route recommendation and congestion alerts
Standard setting: 5-minute steps, T = 12 (the past hour) and T' = 12 (the next hour), reported at 15, 30 and 60 minutes.
Notes: Formal statement: given the past T time steps of speed at N road stretches, predict the next T' steps at all N. Then the optimisation half: convert predicted speed to travel time per road (length divided by speed), run Dijkstra on those times, and recommend the fastest route; the same forecasts give congestion alerts when predicted speed falls well below the free-flow speed.

## Slide 6: Objectives
1
Build the dataset
Public benchmarks (METR-LA, PEMS-BAY) plus our Bengaluru Outer Ring Road corridor: 21 stretches, with weather and incidents.
2
Model the road network
Stretches as nodes, drivable links as directed edges, with OpenStreetMap features such as signals, lanes and speed limits.
3
Forecast speed
Predict 15, 30 and 60 minutes ahead; compare Historical Average, XGBoost, LSTM, Graph WaveNet and STID.
4
Evaluate fairly
Chronological split, masked MAE, RMSE and MAPE at every horizon, so every claim can be checked.
5
Flag congestion
Compare predicted speed with each road's free-flow speed to give early warnings.
6
Recommend routes
Cost = length ÷ predicted speed; Dijkstra picks the fastest route, shown on a map dashboard through an API.
Notes: Six objectives, each testable. 1 and 2 are data and graph; 3 and 4 are the forecasting study and how it is judged; 5 and 6 are the congestion optimisation, delivered as alerts and route recommendation.

## Slide 7: Literature Survey 1: Graph Models
Work | Key idea | Gap it leaves
STGCN (Yu et al., IJCAI 2018) | Graph convolution for space plus gated temporal convolution; fully convolutional and fast to train. | Fixed distance-based graph; needs many layers for long histories.
DCRNN (Li et al., ICLR 2018) | Diffusion convolution on directed roads inside a GRU encoder-decoder; released METR-LA and PEMS-BAY. | Recurrent: slow to train and errors build up over steps.
ASTGCN (Guo et al., AAAI 2019) | Spatial and temporal attention; uses recent, daily and weekly input segments. | Needs three input windows, so heavier data preparation.
Graph WaveNet (Wu et al., IJCAI 2019) | Learns an adaptive adjacency matrix from node embeddings; dilated causal convolution. | Learned graph is fixed once training ends.
GMAN (Zheng et al., AAAI 2020) | Attention-based encoder-decoder with spatio-temporal embeddings; strong at long horizons. | Attention cost grows with network size.
AGCRN (Bai et al., NeurIPS 2020) | Node-specific parameters and a learned graph; needs no predefined road graph. | Learned graph ignores real road distance.
Notes: Walk down the table: each paper fixes a weakness of the one before. STGCN made it convolutional and fast; DCRNN handled directed roads with diffusion but is recurrent; ASTGCN added attention and periodic inputs; Graph WaveNet learns the graph; GMAN uses attention for long horizons; AGCRN needs no predefined graph. Venues are on the slide; full references are on the last slide.

## Slide 8: Literature Survey 2: The Numbers
Chart: METR-LA: MAE in mph (lower is better)
| ARIMA | FC-LSTM | STGCN | DCRNN | Graph WaveNet
15 min | 3.99 | 3.44 | 2.88 | 2.77 | 2.69
60 min | 6.9 | 4.37 | 4.59 | 3.6 | 3.53
Source: Wu et al., Graph WaveNet, IJCAI 2019, Table 2 (207 sensors, 5-minute data).
Error grows with horizon
ARIMA rises from 3.99 to 6.90 mph; Graph WaveNet from 2.69 to 3.53.
Network-aware models win
DCRNN and Graph WaveNet cut the 60-minute error to about half of ARIMA's.
The graph can be learned
Graph WaveNet's adaptive-only graph (MAE 3.10) matches the distance-based one (3.13).
Notes: Numbers are as reported in the Graph WaveNet paper, Table 2, on METR-LA. Three lessons: error grows with horizon; models that use the road network roughly halve the 60-minute error of ARIMA; and a graph learned from data performs about as well as the distance-based graph, which matters for us because our own corridor graph is small and built from map data.

## Slide 9: Literature Survey 3: Recent Work
STID (Shao et al., CIKM 2022)
A plain MLP with spatial and time-of-day embeddings rivals complex graph models.
STAEformer (Liu et al., CIKM 2023)
A vanilla transformer with spatio-temporal adaptive embeddings; a strong recent baseline.
PDFormer (Jiang et al., AAAI 2023)
Models propagation delay: a jam takes time to travel from one road to the next.
LargeST (Liu et al., NeurIPS 2023)
Benchmark of about 8,600 California sensors for large-scale forecasting tests.
ST-ResNet (Zhang et al., AAAI 2017)
City grid crowd flows with external factors such as weather and holidays.
IntelliLight (Wei et al., KDD 2018)
Reinforcement-learning signal control; needs a simulator, so we chose route recommendation.
Where this project fits: strong simple baselines first (Historical Average, LSTM, STID), then Graph WaveNet, on a connected Bengaluru corridor, with forecasts feeding route recommendation.
Notes: Recent work shows simple models with good embeddings rival complex graph networks, so we compare against STID and do not claim a new architecture. PDFormer adds propagation delay, ST-ResNet shows external factors such as weather help, LargeST is the large benchmark. IntelliLight is the reinforcement-learning signal-control line; it needs a simulator and urban intersection data, which is why we chose route recommendation for the optimisation half.

## Slide 10: Progress So Far and Next Steps
Done
Problem scoped and literature reviewed
Data collector running 24/7 since 27 September 2026 (speeds, weather)
Corridor of 21 connected stretches with links and OpenStreetMap features
Incident feed added to the collector
Next
Reproduce baselines on METR-LA (Historical Average, LSTM, Graph WaveNet)
Train on 4 to 6 weeks of Bengaluru data
Build congestion alerts and route recommendation
Map dashboard and final evaluation
Notes: Status for Phase-1: scope and literature are done; the data pipeline is already collecting; the corridor graph and incident feed are built. Next phase: baselines, training on the Bengaluru data, alerts and routing, dashboard.

## Slide 11: References
1. Y. Li, R. Yu, C. Shahabi, Y. Liu. Diffusion Convolutional Recurrent Neural Network: Data-Driven Traffic Forecasting. ICLR 2018.
2. B. Yu, H. Yin, Z. Zhu. Spatio-Temporal Graph Convolutional Networks: A Deep Learning Framework for Traffic Forecasting. IJCAI 2018.
3. Z. Wu, S. Pan, G. Long, J. Jiang, C. Zhang. Graph WaveNet for Deep Spatial-Temporal Graph Modeling. IJCAI 2019.
4. S. Guo, Y. Lin, N. Feng, C. Song, H. Wan. Attention Based Spatial-Temporal Graph Convolutional Networks for Traffic Flow Forecasting. AAAI 2019.
5. C. Zheng, X. Fan, C. Wang, J. Qi. GMAN: A Graph Multi-Attention Network for Traffic Prediction. AAAI 2020.
6. L. Bai, L. Yao, C. Li, X. Wang, C. Wang. Adaptive Graph Convolutional Recurrent Network for Traffic Forecasting. NeurIPS 2020.
7. Z. Shao, Z. Zhang, F. Wang, W. Wei, Y. Xu. Spatial-Temporal Identity: A Simple yet Effective Baseline for Multivariate Time Series Forecasting. CIKM 2022.
8. H. Liu et al. STAEformer: Spatio-Temporal Adaptive Embedding Makes Vanilla Transformer SOTA for Traffic Forecasting. CIKM 2023.
9. J. Jiang, C. Han, W. X. Zhao, J. Wang. PDFormer: Propagation Delay-Aware Dynamic Long-Range Transformer for Traffic Flow Prediction. AAAI 2023.
10. X. Liu et al. LargeST: A Benchmark Dataset for Large-Scale Traffic Forecasting. NeurIPS 2023, Datasets and Benchmarks.
11. J. Zhang, Y. Zheng, D. Qi. Deep Spatio-Temporal Residual Networks for Citywide Crowd Flows Prediction. AAAI 2017.
12. H. Wei, G. Zheng, H. Yao, Z. Li. IntelliLight: A Reinforcement Learning Approach for Intelligent Traffic Light Control. KDD 2018.
13. TomTom Traffic API documentation (Flow Segment Data, Incident Details): docs.tomtom.com.
14. OpenStreetMap contributors, data under the Open Database Licence (ODbL).
Notes: Reference list for the literature survey. Results quoted on the chart slide come from reference 3, Table 2.